## Slide 1
TEMPORAL VISUAL REUSE IN OPENVLA-OFT
A sequential negative study of caching across robot-control queries
Ved Dwivedi¹ | Cheng Yang² | Bo Yuan²
¹ John P. Stevens High School ² Department of Electrical and Computer Engineering, Rutgers University-New Brunswick
RUTGERS
UNIVERSITY
RESEARCH QUESTION
Can a frozen robot policy reuse visual computation across queries without losing task success?
SHORT ANSWER
Not under the tested designs: savings and reliability did not coexist.
FIVE INCREASINGLY TARGETED TESTS
Each redesign addressed the failure observed in the preceding stage.
SAVR
reuse both
cameras
ACR
keep wrist
current
BRACE
reuse selected
K/V groups
PAIR
predict reuse
risk
CAC
correct cached
actions
Test bed: OpenVLA-OFT on LIBERO | terminal task success + complete-query timing | frozen gates and independent semantic checks
RESULTS: COMPUTE SAVINGS APPEARED, BUT NO METHOD PASSED BOTH GATES
1 More reuse generally reduced success
0
10
20
30
40
50
60
70
80
90
0
20
40
60
80
100
Terminal success (%)
Online visual or scene reuse (%)
98% reference
SAVR1
SAVR2/3
ACR
High-success safeguards worked only by suppressing reuse. The strongest SAVR redesign reached 69/70 success but reused just 0.95% of visual queries.
2 Camera asymmetry preserved success - not speed
Chart: Wall time (ms/query)
| Sequential FR | Batched FR | ACR
Wall time | 1240.04 | 1188.28 | 1190.97
67/70 = 67/70
ACR success = batched full refresh
3 The final cache substrate failed closed-loop control
Chart: Terminal success (%)
| Dense | Balanced recursive cache
Terminal success | 56.67 | 0
Dense: 68/120 successes | Cache: 0/120 | 22.60% gross timing headroom in systems qualification
CORE FINDING | Useful compute savings appeared, but no tested frozen-model method achieved both reliability and incremental speed.
WHY CLOSED-LOOP REUSE IS HARD
Recursive reuse combines internal states from different physical times. A changed action changes the next observation, so offline replay misses the feedback loop.
CURRENT
IMAGES
MIXED-AGE
K/V STATE
ACTION
DEVIATION
NEW ROBOT
STATE
NEXT CACHE
DECISION
feedback compounds across control queries
WHAT THE STUDY CONTRIBUTES
1
Optimize the fresh baseline first
Batching erased ACR's apparent speedup.
2
Check model semantics independently
Shared helper code hid a one-token action-readout error.
3
Test closed loop early
Offline similarity and risk signals did not guarantee control.
4
Next direction
Preserve current task-critical information or train the model under reuse.
SCOPE | One OpenVLA-OFT checkpoint, one simulator benchmark family, one GPU class. Cross-stage comparisons are descriptive, not randomized head-to-head estimates.
Key references: OpenVLA (CoRL 2024); OpenVLA-OFT (RSS 2025); VLA-Cache (NeurIPS 2025); LIBERO (NeurIPS 2023).
CODE + ARTIFACTS
github.com/vwdr/SAVR
Notes: [Sources]
- Project results and wording: /Users/veddwivedi/Documents/VLA/SAVR/output/pdf/Temporal_Visual_Reuse_in_OpenVLA_OFT_A_Sequential_Negative_Study.pdf
- MIT URTC poster guidance: https://urtc.mit.edu/poster_presentation_2024.pdf
- Rutgers visual identity: https://communications.rutgers.edu/services-resources/logos-signatures-and-visual-identity
- Rutgers logo image: https://communications.rutgers.edu/sites/default/files/lg_rutgers_signature_samples2.png
- Repository QR target: https://github.com/vwdr/SAVR
[/Sources]